## Slide 1: EE 305 project
Group 9

## Slide 2
Group Members:
Harshitha Budati 200002022
K Sneha 200002041
Pavani Oruganti 200002057
Sarvani V S 200002068
Kirtika Zanzan 200002085

## Slide 3: Problem Statement
Consider a plane wave (having angular frequency of w rad/sec and phase constant of 𝛃 rad/m) propagating along a transmission line and terminated by a load impedance ZL. The
transmission line has a characteristic impedance of Zo (=Ro + jXo) and length of l. Plot the input
impedance Zi of the transmission line for different values of the load impedance ZL (=RL + jXL). Note:
the parameter l should be considered as input in terms of 𝛌. The parameter values 𝛃, w, l, R0, X0, RL,
XL will be provided from user-end.

## Slide 4: THEORY
The propagation constant for a TEM wave is
Ɣ = 𝝰+ j 𝛃
Where 𝝰 is attenuation factor and 𝛃 is phase shift constant.
The formula for the input impedance Zi of a lossless line of length l terminated in ZL
Equation (I)
In most cases transmission-line segments can be considered lossless. i.e. 𝝰 = 0
Hence, Ɣ = j𝛃, Z0 = R0, and tanh Ɣl = tanh (j𝛃l) = j tan 𝛃l
The equation (I) becomes
Equation (II)

## Slide 5
We now consider several important special cases.
1. Open-circuit termination (ZL →∞)
  We have, from Eq. (II),
  Equation (III)
  Above equation shows that the input impedance of an open-circuited lossless line is purely reactive. The line can, however, be either capacitive or inductive because the function cot 𝛃l can be either positive or negative, depending on the value of 𝛃l(=2𝞹l/𝛌).
  Input reactance of open-circuited transmission line

## Slide 6
2. Short circuit (ZL=0)
  We have, from Eq. (II),
  Equation (IV)
  Since tan 𝛃l can range from -∞ to +∞, the input impedance of a short-circuited lossless line can also be either purely inductive or purely capacitive, depending on the value of 𝛃l
  Input reactance of short-circuited transmission line

## Slide 7
3. Quarter-wave sections (l = 𝞴/4, 𝛃l= 𝞹/2)
  When the length of a line is an odd multiple of 𝞴 /4, l = (2n-1)𝞴/4, (n = 1,2,3, . .)
  And eq(I) becomes
  Quarter-wave line
  Hence, a quarter-wave lossless line transforms the load impedance to the input terminals as its inverse multiplied by the square of the characteristic resistance; it is often referred to as a quarter-wave transformer.

## Slide 8
4. Half-wave sections (l = 𝞴/2, 𝛃l= 𝞹)
  When the length of a line is an integral multiple of 𝞴/2, l = n𝞴/2 (n = 1, 2, 3, . . .),
  Thus, eq(I) reduces to
  a half-wave lossless line transfers the load impedance to the input terminals without change.
  We get linear graphs for Zi vs Zl plot in this case.

## Slide 9: RESULTS
Lossless Case 𝝰 = 0:
1. Short circuit case (ZL=0)

## Slide 10
2. Quarter-wave sections (l = 𝞴/4, 𝛃l= 𝞹/2)

## Slide 11
3. Half-wave sections (l = 𝞴/2, 𝛃l= 𝞹)

## Slide 12
CONCLUSION
We’ve seen how transmission lines behave in different conditions such as lossless/lossy and also in different lengths of sections into consideration.
REFERENCES
1. Lecture Notes
2. David K. Cheng : Fields and elctromangnetics

## Slide 13
THANK YOU